## Slide 1: Estimating the Effects of Operational Strategies on Travel-Time Reliability for Smart Mobility
Eil Kwon and Chongmyung Park
University of Minnesota Duluth
Avinash Sankarasetty, Kaushik Ayinala, and Sejun Song
School of Computer and Engineering (SCE)
University of Missouri - Kansas City, USA

## Slide 2: Outline
Background
Research Objectives
Development of Travel-Time Reliability Estimation System (TeTRES)
TeTRES Case Studies
Future Work

## Slide 3
Smart City Infrastructures
Smart
Mobility
Smart
Utilities
Smart
Buildings
Smart
Governance
Efficient, Safe and Environmentally Friendly Mobility Service
A ‘Reliable’ Roadway Network
‘Travel-Time Reliability’ => A Key Performance Measure of
Smart Mobility Service
Background

## Slide 4: Average Travel Time
Most travelers are less tolerant of unexpected delays and tend to remember the few bad days
Most concern of travelers, cannot be measured by simple ‘Average’
Source: FHWA, US DOT
How traffic conditions have been communicated
Annual average
Travel Time
Jan July Dec
What travelers experience …
… and what they remember
Travel times vary greatly day-to-day
Jan July Dec
Travel Time
“Travel Time Reliability presents the consistency or dependability in Travel Times, as measured from day-to-day and/or across different times of the day.”

## Slide 5: Travel Time Reliability
Measures the extent of ‘unexpected delay’
Captures the benefit of transportation system management/operations
Reflects the improvements of worst conditions
Source: FHWA, US DOT
Travel Time
2014 2015 2016
Small improvement in average travel times
Large improvement in travel time reliability
Travel Time
2014 2015 2016

## Slide 6: Measuring Travel Time Reliability
Considering unexpected delays
90th or 95th percentile travel times estimates how bad delay will be on specific routes during the heaviest traffic days.
Buffer index is the additional time
  Travelers must add to their average travel time when planning trips to ensure on-time arrival 95 percent of the time.
  i.e., 95 percent average travel time is 20 min, buffer index is 40 percent, then buffer time is 8 min  28 mins.
Planning time index represents how much total time
  A traveler should allow to ensure on-time arrival.
  i.e., free-flow travel time is 15 min, planning time index is 1.6, then planning time is 8 min  24 mins.

## Slide 7
Building a framework to estimate and analyze travel-time reliability for given corridors/time periods by applying various unexpected delays
  Integration of traffic, incident, weather, work zone, special event, and snow maintenance condition
  Automation of processes for data collection, reliability estimation, reporting functions
  Support for driver information system by providing expected, e.g., 95th %-ile, travel time for user-selected corridors
Research Objectives

## Slide 8: Travel-Time Reliability Estimation / Analysis System (TeTRES)
Demand Variations/Geometry
Weather
Incident
Work zone
Special Event
Road Surface Condition

## Slide 9: Vehicle Trajectory Identification with the Speed Data from Loop Detectors
Space
Station 1
t1
t2
t3
t4
t5
Time
t0
Station 2
Station 3
Station 4
traffic flow
direction
u2
u3
(u2+u3)/2
d2,3
d2,3 / 3
d2,3 / 3
d2,3 / 3
Travel Time from Station 1 to Station 4 at t0

## Slide 10: TeTRES System Architecture
Identifying the Effects of Individual or Combined Factors on Reliability
=> Critical in Developing Effective Operations/Planning Strategies

## Slide 11: Travel-Time Reliability Estimation Client Panel

## Slide 12: Applying Unexpected Conditions to Reliability

## Slide 13
Case Studies
TeTRES case studies on Minnesota Network to estimate effects of operational changes on reliability measures
  Case 1: Effects of adaptive ramp metering strategy on corridor reliability
  Case 2: Effects of aggressive incident management on corridor / network reliability

## Slide 14
Effects of Adaptive Ramp Metering on Corridor Reliability
(169 SB, Twin Cities, Minnesota)
* Planning Time Index = 95th %ile TT / Free-Flow TT
Case 1: Ramp metering effect

## Slide 15
Corridor reliability during 2018 Super-Bowl Period, Minneapolis, Minnesota
Case 2: Aggressive incident management effect

## Slide 16
Network-wide Reliability Variations during Super-Bowl Period
Case 2: Aggressive incident management effect

## Slide 17
Full automation of data input process
  e.g., work-zone lane-configuration data
Identification and modeling of causal relationships between reliability and geometric/operational changes on a corridor and network level
Development of measures for corridor/network-wide operational resiliency
Work in Progress